## Slide 1
OGC API DGGS - Background
Robert Gibb
119th OGC Member Meeting
Virtual | 16 June 2021

## Slide 2: OGC API DGGS
OGC Abstract Specification 21 v 2.0 DGGS: https://github.com/opengeospatial/ogcapi-discrete-global-grid-systems/blob/master/20-040r3-OGC-AS21-DGGSv2.0-draft-19170-1-proof.pdf c.f. section 8.3.3. Core Topological Query Functions module
Defines ZoneQuery operations which are redefined from Query2D and Query 3D ISO 19107:2019 Spatial Schema – these are DE9IM operations: within, crosses, union etc
Three critical differences are introduced in ZoneQuery:
  Geometries in ZoneQuery are represented by Zonal Identifiers, rather than by sets of coordinates in Query2D and Query3D,
  A single set of operations now cover 1D, 2D, 3D & 4D topological queries, this is achieved through a projectTo parameter, which controls the dimensionality of the operation, which is less than or equal to the dimensionality of the zones being compared.
  The operations are all defined as topological comparisons between two zones, rather than two features. With DGGS all features are represented by lists of Zonal Identifiers, so features can be compared topologically as a result of recursively applying the zone level comparisons to all the members in the list. So a second level of topological operators are implied by the standard, that operate on lists.

## Slide 3: DGGS – RS Navigator: topological functions on ZoneID
<<query>> (1D) relativePosition(another:ZonalIdentifier, projectTo:DirectPosition[4])
<<query>> contains (another:ZonalIdentifier, projectTo:DirectPosition[4])
crosses (another:ZonalIdentifier, projectTo:DirectPosition[4])
disjoint (another:ZonalIdentifier, projectTo:DirectPosition[4])
equals (another:ZonalIdentifier, projectTo:DirectPosition[4])
intersects (another:ZonalIdentifier,projectTo:DirectPosition[4])
overlaps (another:ZonalIdentifier, projectTo:DirectPosition[4])
touches (another:ZonalIdentifier, projectTo:DirectPosition[4])
within (another:ZonalIdentifier, projectTo:DirectPosition[4])
withinDistance(another:ZonalIdentifier, dist:Distance, projectTo:DirectPosition[4])
parentOf (another:ZonalIdentifier, inheritID:Boolean, projectTo:DirectPosition[4])
childOf (another:ZonalIdentifier, inheritID:Boolean, projectTo:DirectPosition[4])
siblingOf (another:ZonalIdentifier, inheritID:Boolean, projectTo:DirectPosition[4])
<<set>> buffer (dist:Distance, projectTo:DirectPosition[4])
difference (another:ZonalIdentifier, rangeRefine:refinementLevelRange, projectTo:DirectPosition[4])
intersection (another:ZonalIdentifier, rangeRefine:refinementLevelRange, projectTo:DirectPosition[4])
symDifference(another:ZonalIdentifier,rangeRefine:refinementLevelRange, projectTo:DirectPosition[4])
union (another:ZonalIdentifier, rangeRefine:refinementLevelRange, projectTo:DirectPosition[4])
parent (inheritID:Boolean, levels:Integer, projectTo:DirectPosition[4])
child (inheritID:Boolean, levels:Integer, projectTo:DirectPosition[4])
sibling (inheritID:Boolean, levels:Integer, projectTo:DirectPosition[4])
<<reference>> (1D) relatePosition(another:ZonalIdentifier, relate:RelativePosition, projectTo:DirectPosition[4])
<<reference>> relate (another:ZonalIdentifier, matrix:CharacterString, projectTo:DirectPosition[4])

## Slide 4: DGGS – RS Navigator: topological function parameters
another:ZonalIdentifier Specifies the target region for the query. In zonal query a zone's identifier provides suﬀicient (Mandatory) description of its topology. ZonalIdentifier takes the place of the geometry data used in Query2D and Query3D for both the source and the target.
projectTo:DirectPosition[4] projectTo specifies an optional reference direction, surface or volume for an operation.
(Optional, default:(1,1,1,1) ) Allowed values for each direction are 0 and 1, and spatial directions may also have a value of n.
projectTo defines a vector whose starting point is inferred as the point with each projectTo direction whose value is 1 set to 0. It takes one of three forms:
1D: In its one-dimensional form for specifying a reference direction, one direction has a value of 1. For example, (0,0,0,1) projects to the temporal axis, and (0,0,1,0) projects to the vertical axis.
Only the 1D form is supported by relativePosition and relatePosition, default (0,0,0,1).
2D: In its two-dimensional form for specifying a reference surface, two directions have a value of 1. For example, a surface at height n is specified by a projectTo value of (1,1,n,0) representing the vector [ (0,0,n,0), (1,1,n,0) ].
3D: In its three-dimensional form for specifying a reference volume, three directions have a value of 1. For example, (1,1,1,0) projects to a spatial volume without reference to time, and (1,1,n,1) projects to a surface spanning all time at height n.

## Slide 5: DGGS – RS Navigator: topological functions parameters (cont)
rangeRefine:refinementLevelRange Specifies the range of refinement levels to include in a return <<set>>. (Optional, default: [min:max]) The lower and upper bounds in the refinementLevelRange datatype are both included in the range.
levels:Integer Levels indicates the relative number of levels in the hierarchy to be traversed in assembling a (Optional, default:1) result <<set>>
inheritID:Boolean When inheritID has a value of True the result <<set>> only contains cells for which the IDs (Optional, default:False) have shared inheritance, and a value of False indicates that inheritance is ignored.
dist:Distance a distance measure with units.
matrix:CharacterString 3x3 intersection matrix of DE-9IM string codes with values {0,1,2,3,F,*}
relate:RelativePosition a RelativePosition code as defined in W3C/OGC 16-071r3 : {Before, After, Meets, MetBy, Overlaps, OverlappedBy, Starts, StartedBy,
During, Contains, Finishes, FinishedBy, Equals, In, Disjoint}

## Slide 6: DGGS – from Zones to Features (WKT viewpoint)
List of ZoneIDs |  | Directed Lists of ZoneIDs | 
Type | Examples | Type | Examples
OrdinateList set of nD points | POINT, MULTIPOINT | DirectedOrdinateList nD line vertices | LINESTRING, POLYGON (boundary), TRIANGLE, route, trajectory, timeseries
CellList set of nD regions or spaces | POINT, MULTIPOINT, POLYGON, MULTIPOLYGON, point cloud, raster or WMS image, geo-located social media | DirectedCellList nD connected path | route, trajectory, timeseries
TileList set of tiles or ‘b-box’ | TileSet, DB sharding, b-box, jobqueue | DirectedTileList sequence of ‘bbox’ | ordered jobqueue
ZoneCollection collection of other type(s) | MULTILINESTRING, GEOMETRYCOLLECTION | DirectedZoneCollection graph or connected collection of similar or different type(s) | TIN, network (of DirectedOrdinateList or DirectedCellList)
optional | sort by decreasing size, compress |  | 

## Slide 7: DGGS – RS Navigator: topological functions on ZoneID
From single zone topology operations to feature topology operations, do we need anything new?
(List of A).equals(List of B) is True if
the lists are of the same length, and
every member of A can be paired with EXACTLY one member of List B that it is equal to.
Noting that to answer in the negative we only need to find one false match.
With DGGS we have an additional possibility at the feature level, we can add an additional parameter to control the precision of the match, eg rangeRefine:refinementLevelRange
(List of A).equals(List of B, rangeRefine:refinementLevelRange)

## Slide 8
OGC API DGGS - Background
Robert Gibb
119th OGC Member Meeting
Virtual | 16 June 2021

## Slide 9: OGC API DGGS
The DGGS Abstract Specification 21 v2.0 contains definitions for a suite of 4D topological operations that we are going to represent in SwaggerHub as an OpenAPI description.
Practical work: Describing OGC API – DGGS DE9IM <<query>> operations in YAML
Query operations follow the pattern: zone.query-op(another-zone,projectTo) and return True/False (13:15 - 13:45 - 30 minutes)
Practical work: Describing OGC API – DGGS DE9IM <<set>> operations in YAML
Set operations follow the pattern zone.set-op(another-zone,rangeRefine,projectTo) and return a set or list of zones (13:45 – 14:15 - 30 minutes)
Practical work: Describing OGC API – DGGS <<reference>> and DGGS operations in YAML
Reference operations follow the pattern zone.ref-op(another-zone,reference,projectTo) and return True/False also distance, parent, child, sibling, parentOf, childOf, siblingOf (14:15 – 14:45 - 30 minutes)

## Slide 10: OGC API DGGS
Abstract Specification: https://github.com/opengeospatial/ogcapi-discrete-global-grid-systems/blob/master/20-040r3-OGC-AS21-DGGSv2.0-draft-19170-1-proof.pdf c.f. section 8.3.3. Core Topological Query Functions module
TB-16 OGC API – DGGS-Process: https://app.swaggerhub.com/apis/aaime-sh/dggs-process/0.0.3 this is going to be our starting point, it implements many contextual functions for DGGS, and binds to H3 & to rHEALPix implementations, but only 2x of the 24x operations specified in section 8.3.3 are defined, and only in their 2D form. We aren’t going to implement H3 or rHEALPix bindings.
GitHub: https://github.com/opengeospatial/ogcapi-discrete-global-grid-systems

## Slide 11: Requirements
Familiarity with git (clone, etc.)
Familiarity with YAML
Familiarity with github &/or swaggerhub

## Slide 12: OGC API DGGS <<query>>
OGC API DGGS <<query>>
#OGCAPI

## Slide 13: OGC API – DGGS DE9IM <<query>> operations in YAML
Overview
DE9IM <query-op> are: contains, crosses, disjoint, equals, intersects, overlaps, touches, within, withinDistance, relativePosition
General pattern: zone:ZonalIdentifier.<query-op> (another:ZonalIdentifier,projectTo:DirectPosition[4]), return True/False
Variations: zone:ZonalIdentifier.withinDistance (another:ZonalIdentifier,dist:Distance,projectTo:DirectPosition[4]), return True/False zone: ZonalIdentifier.relativePosition (another:ZonalIdentifier,projectTo:DirectPosition[4]), return RelativePosition where RelativePosition:{Before, After, Meets, MetBy, Overlaps, OverlappedBy, Starts, StartedBy, During, Contains, Finishes, FinishedBy, Equals, In, Disjoint}

## Slide 14: OGC API DGGS <<set>>
OGC API DGGS <<set>>
#OGCAPI

## Slide 15: OGC API – DGGS DE9IM <<set>> operations in YAML
Overview
DE9IM <set-op> are: buffer, difference, intersection, symDifference, union
General pattern: zone:ZonalIdentifier.<set-op> (another:ZonalIdentifier,rangeRefine:refinementLevelRange, projectTo:DirectPosition[4]), return a set or list of zones where refinementLevelRange is [maxRefinementLevel:minRefinementLevel]
Variations: zone:ZonalIdentifier.buffer (dist:Distance,projectTo:DirectPosition[4]), return a set or list of zones

## Slide 16: OGC API DGGS <<reference>> etc
OGC API DGGS <<reference>> etc
#OGCAPI

## Slide 17: OGC API – DGGS DE9IM <<reference>> and DGGS operations in YAML
Overview
DE9IM <reference-op> are: relate, relatePosition
DGGS-query operations are: parentOf, childOf, siblingOf
DGGS-set operations are: parent, child, sibling
Other operations are: distance

## Slide 18: OGC API – DGGS DE9IM <<reference>> and DGGS operations in YAML
Overview
DE9IM <reference-op> are: relate, relatePosition
General pattern: zone:ZonalIdentifier.<reference-op> (another:ZonalIdentifier, reference, projectTo:DirectPosition[4]), and return True/False
Variations: for relate reference is a matrix:CharacterString representing a 3x3 Intersection matrix in DE-9IM string codes form where the members have values {0,1,2,F,*} for relatePosition reference is relate:RelativePosition where RelativePosition:{Before, After, Meets, MetBy, Overlaps, OverlappedBy, Starts, StartedBy, During, Contains, Finishes, FinishedBy, Equals, In, Disjoint}

## Slide 19: OGC API – DGGS DE9IM <<reference>> and DGGS operations in YAML
Overview
DE9IM DGGS-query operations are: parentOf, childOf, siblingOf
General pattern: zone:ZonalIdentifier.<dggs-query-op> (another:ZonalIdentifier,inheritID:Boolean,projectTo:DirectPosition[4]), return True/False

## Slide 20: OGC API – DGGS DE9IM <<reference>> and DGGS operations in YAML
Overview
DGGS-set operations are: parent, child, sibling
General pattern: zone:ZonalIdentifier.<dggs-set-op> (another:ZonalIdentifier, inheritID:Boolean, levels:Integer, projectTo:DirectPosition[4]), return a set or list of zones

## Slide 21: OGC API – DGGS DE9IM <<reference>> and DGGS operations in YAML
Overview
other operations are: distance
General pattern: zone:ZonalIdentifier.distance (another:ZonalIdentifier, projectTo:DirectPosition[4]), return a Distance